## Slide 1
EO
OPTIMIZER
PIPELINE
Industrial AI
Kedro Framework
Energy Optimization
Energy Optimization
Pipeline Architecture
Two Philosophies: GenAI-Powered & Configuration-Driven
Architecture Blueprint based on Kedro orchestration, MINLP + Bayesian Optimization, DAG-based inferred tag engine,
configuration-first design and full alignment with the product coding standards.
3,763
PI Tags
41
Config Tables
8
Pipeline Stages
2
Philosophies
5
Boilers / SEUs
Confidential — Technical Architecture Document | 2025

## Slide 2
01
System Context: What We're Optimizing
ETH
Ethylene
7 Furnaces
H-1111 to H-1117
EOEG 1
EO/EG Plant
EG1 Units
KM-2115, E-2531...
EOEG 2
EO/EG Plant
EG2 Units
KM-4115, E-4531...
EOEG 3
EO/EG Plant
EG3 Units
KM-6115, E-6531...
LAO
Plant
LAO Heater
Fuel Gas Opt.
Utility Hub — Optimized Resource:
• HP Steam (BLR 1-5)
• MP Steam
• LP Steam
• BFW (BFW Pumps A-F)
• VHP Steam
• Air (4 Compressors)
• Cooling Water
• DM Water
• Power
Key Configuration Tables (from EO Feature File)
tag
3,763 rows
PI tags + inferred tags registry
inferred_details
2,864 rows
Formula expressions for calculated tags
constraints
33 rows
Mass/energy balance & capacity constraints
variables
142 rows
Optimizer variables with bounds (int/continuous)
derived_equations
92 rows
Pre-optimizer derived tag equations
derived_equation_post_optimizer
86 rows
Post-optimizer computed tags
sub_model
126 rows
Equation & ML sub-models (ordered execution)
seu_detail
59 rows
Specific Energy Units per equipment
objective
1 row
Minimize Objective_2 (Total Operating Cost)
case_configuration_portal
108 rows
Tag quality checks: NaN/stuck/out-of-bound

## Slide 3
02
8-Stage Pipeline Architecture — Common Foundation
Both philosophies share this identical pipeline structure. Only the tag onboarding layer (Step 1) differs.
📡
01
Ingestion
PI / Mock Data
data_ingestion_get_pi_data
Pull PI historian data for case_id+timestamp. Validate availability flag. Apply pipeline_macros (1h interval, 1d window).
🔍
02
CCP Quality
Check
Tag Validation
data_enrichment_pi_tag_imputation
Apply case_configuration_portal rules: NaN check, stuck check, out-of-bound check. Overwrite with defaults where configured.
⚙️
03
Inferred Tag
Engine
DAG + fsolve
data_enrichment_inferred_calculation
Calculate inferred tags via df.eval(). DAG topological sort via NetworkX. Fixed-point iteration (scipy.fsolve) for circular refs (A=f(B), B=f(A)).
🧮
04
Sub-Model
Execution
Equation / ML
pre_optimizer_iterative_inferred
Execute sub_model table in order column sequence. Supports: equation (df.eval), ML regression, iterative fixed-point models.
⛓️
05
Constraint
& Variable Prep
MINLP Input
optimizer_model_preprocessing
Build variables dict (lb/ub/iv/integer) from variables table. Evaluate bound expressions. Load constraints from constraints table. Assemble objective from objective table.
🚀
06
Optimizer
GEKKO / BoTorch
optimizer_model_main
Primary: GEKKO MINLP solver. Proposed upgrade: Bayesian Optimization (BoTorch) for non-convex surfaces. Fallback MINLP for hard constraint sub-problems.
📐
07
Post-Optimizer
Calculations
Derived + Inferred
post_optimizer_inferred_calculation
Calculate derived_equation_post_optimizer tags. Re-run inferred pipeline on optimum data. Merge actual + optimum for opportunity tags (actual - optimum).
📊
08
ODS &
DB Output
Reporting
optimizer_model_inferred_calculation
Generate ODS messages (cause-effect mapping). Compute SEU actual/optimum/baseline/gain/EnPI. Write output to model_output and model_alert_output tables.
Kedro Orchestration Layer:
Each stage = a Kedro micro-pipeline (nodes.py + pipeline.py). Stages are orchestrated by runner.py in the macro-pipeline. Conditional execution supported via global config (e.g., impute: False skips Stage 03). All stage inputs/outputs are Kedro DataSets — no direct DB calls inside nodes.
RM Block names from EO Feature File | Each stage maps 1:1 to rm_blocks table

## Slide 4
03
Philosophy 1: Configuration-Driven (Non-GenAI)
Core Idea:
Engineers provide PI tag lists via the EO feature file (Excel/DB). All tag types, formulas, constraints, variables, and objectives live in config tables — nothing hardcoded in Python. The Kedro pipeline executes deterministically.
A
Tag Configuration Input
tag + inferred_details tables
Engineer populates EO feature file:
• tag table: tag_name, pi_name, tag_type (pi/inferred/constant)
• inferred_details: formula_expression using df.eval() syntax
• model_tag: design_expression, polarity, flag_parameter, flag_ma
Loaded via load_config_from_db(case_id) → injected as Kedro params.
B
DAG-Based Formula Execution
NetworkX topological sort + fsolve
1. Build dependency graph: parse [tag] references in formula expressions
2. nx.is_directed_acyclic_graph(G) — raise exception on cycles
3. nx.topological_sort(G) — auto-resolve execution order
4. Circular refs flagged for fixed-point iteration block (scipy.fsolve)
5. df.eval(formula) per tag in sorted order — zero manual ordering
C
CCP Quality Check Engine
case_configuration_portal per tag
Per tag, evaluate 4 switch types:
• tag_nan_switch: skip/default_warning/default_no_warning
• tag_stuck_switch: no_check/default_warning/value_warning
• tag_out_of_bound_switch: no_check/skip/bound_warning/default
• default_switch: default_warning/default_no_warning
Overwrite bad tags with default_value before optimizer.
D
Variable & Constraint Assembly
variables + constraints tables
Variables: evaluate lower_bound_switch (value/expression), upper_bound_switch, initial_value_switch (actual/lower_bound/last_optimum) → GEKKO m.Var()
Constraints: parse expression strings → m.Equation()
Objective: load objective table (tag_name, direction=-1 for minimize) → m.Obj()
All via df.query() / df.eval() — no hardcoded math.
E
ODS & SEU Output
ods + seu_detail + effect + cause tables
Post-optimizer:
• Compute SEU: actual_duty, target_duty, gain_expression, enpi_expression per equipment
• Evaluate cause expressions → trigger ODS messages with operator text
• Map cause→effect via ods table
• Write to model_output (actual/optimum/polarity/design) and model_alert_output
• Push output PI tags via output_pi_mapping

## Slide 5
04
Philosophy 2: Gen AI-Powered (Document-First Onboarding)
Core Idea:
Engineers upload P&IDs, PFDs, and PI tag lists. A multimodal LLM (Claude / GPT-4o) extracts, classifies, and wires tags automatically. Human-in-the-loop gates validate before config enters production. Once approved, the same 8-stage Kedro pipeline runs identically.
📄
Document Ingestion
Upload P&ID diagrams, PFDs, PI tag sheets as PDF/image. Support: CAD exports, Visio/Lucidchart exports, scanned docs. Stored in document_store with case_id linkage.
🔍
LLM Tag Extraction
Multimodal LLM vision parse:
• Extract instrument tags (PT-101, FT-203, TI-007)
• Classify: Temperature, Pressure, Flow, Level, Status
• Map to equipment / process unit
→ Populates tag table draft (pending review)
🔗
Auto Dependency
Graph
LLM infers process relationships from P&ID topology. NetworkX DAG auto-constructed from extracted connections. No manual wiring. Circular ref detection automatic.
⚙️
Formula Suggestion
Given raw PI tags + process context:
LLM suggests inferred_details formulas.
Example: efficiency = (T_out - T_in) / T_in
→ Engineer reviews in approval UI before DB write.
👁️
Human Review Gate
Approval workflow UI:
• Show extracted tags side-by-side with source diagram
• Accept / Reject / Edit each tag and formula
• Approved → written to EO config tables
• Rejected → flagged for manual entry
🚀
Same 8-Stage
Pipeline Executes
Once config tables are populated (same schema as Philosophy 1), the identical Kedro macro-pipeline runs. GenAI is only in the onboarding layer — core optimization logic is identical.
★ Human review gates are non-negotiable before any LLM-extracted config enters the optimizer. Never trust raw LLM output without engineer sign-off.

## Slide 6
05
Optimizer Strategy: MINLP → Hybrid Approach
Current: GEKKO MINLP
RapidMiner → Python GEKKO
✓ Works well for well-constrained convex problems
✓ Hard constraint guarantees (mass/energy balances)
✓ Proven on ETH furnaces + boiler steam optimization
✗ Struggles with non-convex, noisy furnace surfaces
✗ Requires good initial values — sensitive to IV switch
✗ Max iterations set to 1000 — can fail to converge
✗ Binary integer variables slow branch-and-bound
Proposed: Hybrid Strategy
BoTorch Bayesian Opt + GEKKO fallback
Primary: Bayesian Optimization (BoTorch)
Gaussian Process surrogate model over objective surface. Ideal for non-convex, expensive-to-evaluate furnace simulations. Uncertainty quantification on setpoint recommendations.
Fallback: GEKKO MINLP
For constraint-satisfaction-critical sub-problems where hard algebraic constraint guarantees are required (mass/energy balances). Called when BO solution violates a hard constraint.
Future: RL (PPO/SAC)
For long-horizon control (shift-level). Requires a validated plant digital twin. Phase 3 roadmap after BO deployment and sufficient historical data.
Circular Reference Handling — Fixed-Point Iteration
FROM FLOWCHART + FEATURE FILE | pre_optimizer_iterative_inferred block
Problem: Some inferred tags are mutually dependent — A = f(B), B = f(A). Standard df.eval() cannot resolve these sequentially.
Solution: scipy.optimize.fsolve() solves the system of equations simultaneously. Tags flagged pre_optimizer_iterative_inferred = 1 in inferred_tag_rm_block_mapping table enter this block.
Example from feature file: EOEG_2_MPS_Demand_raw depends on multiple reactor temps, oxygen control, EOE metrics — complex interdependency resolved via fsolve.
SEU (Specific Energy Units) & ODS (Operational Decision Support) Layer
SEU per equipment (59 equipment units): baseline_duty, actual_duty, target_duty, gain_expression, enpi_expression, benefit_factor — written to output PI tags via output_pi_mapping.
ODS: effect (Power_Bill, Fuel_Bill, DMW_Bill) → cause (Boiler_Load_HIGH, Low_Conductivity, Compressor_Efficiency_low) mapping generates actionable operator messages with step change values.
PEEO Adjustment: Efficiency model-based adjustments (peeo_based_adjustment table) feed back into SEU target calculations for each EG unit.

## Slide 7
06
Kedro Module Structure — Node-Level Architecture
Folder Structure
project_root/src/
├── pipelines/
│ ├── macro_pipelines/
│ │ └── eo_optimization/
│ │ ├── pipeline.py
│ │ └── runner.py
│ └── micro_pipelines/
│ ├── ingestion/
│ ├── ccp_quality/
│ ├── inferred_engine/
│ ├── sub_model/
│ ├── optimizer_prep/
│ ├── optimizer/
│ ├── post_optimizer/
│ └── ods_reporting/
├── config/
│ ├── db_loader.py
│ └── catalog.yaml
├── data_access/
│ ├── pi_client.py
│ └── db_client.py
├── orchestration/
│ ├── dag_manager.py
│ └── pipeline_builder.py
└── genai/ ← Phil. 2 only
├── document_parser.py
├── tag_extractor.py
└── review_gateway.py
ingestion/nodes.py
create_pi_connection(pi_config)
fetch_pi_data(pi_conn, tags, window)
standardize_columns(raw_df, mapping)
map_tags(std_df, tag_config)
ccp_quality/nodes.py
check_tag_nan(df, ccp_config)
check_tag_stuck(df, ccp_config, n_hours)
check_tag_out_of_bound(df, ccp_config)
apply_defaults(df, ccp_config)
inferred_engine/nodes.py
build_dependency_graph(inferred_cfg)
detect_circular_refs(G) → fsolve_tags
topological_sort_tags(G)
evaluate_inferred_tags(df, formula_cfg, order)
sub_model/nodes.py
execute_equation_model(df, model_cfg)
execute_ml_model(df, model_cfg, model_file)
run_fixed_point_iteration(df, iter_cfg)
aggregate_sub_model_outputs(df)
optimizer_prep/nodes.py
build_variables(df, var_cfg)
evaluate_bounds(df, var_cfg)
build_constraints(df, const_cfg)
build_objective(df, obj_cfg)
optimizer/nodes.py
run_bayesian_optimizer(vars, obj, const)
run_gekko_minlp(vars, obj, const)
validate_solution(result, const)
format_optimizer_output(result)
post_optimizer/nodes.py
calc_derived_post_opt(df, derived_cfg)
calc_optimum_inferred(df_opt, inferred_cfg)
merge_actual_optimum(df_actual, df_opt)
calc_opportunity_tags(merged_df, pol_cfg)
ods_reporting/nodes.py
compute_seu_metrics(df, seu_cfg)
evaluate_cause_expressions(df, cause_cfg)
generate_ods_messages(causes, effect_map)
write_output_to_db(df, output_cfg)
⚛ Every node: 10-30 lines | Pure function (df.copy()) | Zero furnace-specific logic | Single responsibility | 100% config-driven | No hardcoded tag names

## Slide 8
07
Side-by-Side Comparison & Tech Stack
Dimension
⚙️ Config-Driven (Philosophy 1)
🤖 Gen AI (Philosophy 2)
Tag Onboarding
Manual CSV/DB entry by engineer
Auto-extracted from P&ID via LLM
Formula Generation
Engineer writes formulas in DB
LLM suggests, engineer approves
Dependency Wiring
DAG from inferred_details schema
P&ID topology + LLM inference
Time to New Plant
Days (full tag entry required)
Hours (upload docs → review)
Hallucination Risk
None — engineer owns all logic
Medium — needs review gates
Infrastructure Cost
Low — pure Python, no LLM calls
Higher — LLM API + vision models
Audit Trail
Fully deterministic, traceable
LLM-assisted, gate-controlled
Explainability
Config tables = source of truth
LLM generates NL summaries
Optimizer
GEKKO MINLP → BoTorch BO
GEKKO MINLP → BoTorch BO
Best For
Stable plants, known tag structure
Multi-site rollout, greenfield
Tech Stack
Orchestration:
Kedro 0.19+
Optimizer (Primary):
BoTorch / Optuna
Optimizer (Fallback):
GEKKO / Pyomo
Dependency Graph:
NetworkX
Circular Refs:
scipy.optimize.fsolve
PI Historian:
osisoft.pi / PI Web API
Imputation ML:
LightGBM / scikit-learn
Config Store:
PostgreSQL + YAML
GenAI Layer:
Claude API (claude-sonnet)
Dashboard:
Streamlit / FastAPI
Formula Engine:
pandas df.eval()
Constraint Engine:
pandas df.query()
Non-Negotiable Engineering Standards (from Product Coding Standards Rev 1)
🔒 Everything configurable
Tag limits, formulas, imputation strategies, objective — in DB/YAML. Zero furnace-specific logic in Python.
⚛️ Atomic nodes (10-30 lines)
create_pi_connection ≠ fetch_pi_data ≠ standardize_columns. Never merge responsibilities.
🧪 Pure functions only
Always df.copy(). No side effects. No global state inside nodes. Inputs → outputs only.
🔁 DAG-enforced order
Never manually order formulas. NetworkX topological_sort always. nx.is_directed_acyclic_graph() before execution.
♻️ Composable pipelines
Same preprocessing_pipeline runs on every plant. Only config changes between case_ids.

## Slide 9
Architecture Golden Rules
Summary for Development Teams
🔒
Configuration Is Law
Every tag limit, formula, imputation strategy, constraint expression, and objective function lives in the EO feature file / DB tables. If it's not in config, it doesn't exist. Redeploy for any of these = architecture failure.
⚛️
Nodes Are Atoms
Each Kedro node does exactly one thing. 10-30 lines maximum. create_pi_connection connects. fetch_pi_data fetches. standardize_columns maps. Never combine. If you need to combine, you haven't split enough.
🧪
Pure Functions Only
Every node takes inputs, operates on df.copy(), and returns outputs. No writes to external state. No global mutations. No hidden dependencies. This enables unit testing of every node in complete isolation.
🔁
Let the DAG Decide
Never manually order inferred tag calculations. Build the dependency graph from formula expressions. Let NetworkX topological_sort determine the sequence. Always validate with nx.is_directed_acyclic_graph(). For circular refs, use scipy.fsolve — never loop naively.
♻️
Pipelines Are Reusable Across Plants
The same ingestion_pipeline, preprocessing_pipeline, and optimizer_pipeline run for every case_id. Only load_config_from_db(case_id) changes between sites. Adding a new plant = adding rows to DB tables, not writing Python.
👁️
GenAI Needs Human Gates
LLM-extracted tags and formulas from P&IDs are suggestions, not production config. Every item must pass engineer review before being written to the EO config tables. No direct LLM → optimizer pathway without human validation.
Energy Optimization Pipeline · Kedro + Bayesian Optimization + Configuration-First · Architecture Blueprint